## Slide 1
SR UNIVERSITY • DEPT OF CSE • OS & CN LAB PROJECT (PRODUCT 8)
Industrial Machine Log Integrity Checker
Zero-Dependency Modulo-2 Polynomial Division & Telemetry Error Detection Engine
PRODUCT OVERVIEW
Problem Statement & Objective
• Industrial Context: SCADA, robotics, and PLC telemetry logs are transmitted across noisy industrial lines (RS-485, CAN bus, Modbus TCP) susceptible to electromagnetic noise and tampering.
• Silent Corruption: A single flipped bit alters critical sensor logs (e.g. '8' -> '9' flips TEMP:82.4C to 92.4C), leading to false shutdowns or unflagged catastrophic failures.
• Core Solution: A hardware-deterministic, session-fixed 33-bit CRC-32 polynomial division engine that validates transmission integrity in real time with 100% burst error detection.
• GitHub Repository: https://github.com/rogeralukka/OS-CN-Product-8
TEAM ROLE DISTRIBUTION (GUIDELINE SECTION 10)
Group VIII Members & Demonstration Responsibilities
1. ROGER A RAJU (Lead / Architecture): Problem statement, product overview, software workflow & dataset management (Slide 1 & 2).
2. K. ROHIT GOUD (Algorithms Lead): GF(2) Galois field mathematics, Modulo-2 XOR logic & CRC-32 polynomial division (Slide 3 & 4).
3. G. SIDDHARTHA (Data Ingestion Lead): ASCII-to-binary stream mapping, file input parsing (.log/.txt) & dashboard integration (Slide 4 & 5).
4. P. HARSHAVARDHAN (Backend & Telemetry): Flask REST API (/api/compute, /api/verify), session divisor & live step telemetry (Slide 5 & 6).
5. G. REVANTH (QA & Verification Lead): Test cases (TC-01..TC-05), error-injection simulation, challenges & summary (Slide 7 & 8).

## Slide 2
SLIDE 2 • PRODUCT SUMMARY
Introduction to the Product & Software Workflow
SLIDE 02
Area | What is Implemented in Product 8
Problem Requirement | Detects bit-level telemetry mutations, transmission noise, and log tampering in real-time industrial SCADA systems. CRC is required because additive checksums fail on bit swaps and burst noise.
Implementation Plan | 1. User Input (Text/File) -> 2. ASCII-to-Binary Conversion -> 3. Append 32 Zeros -> 4. Handwritten Modulo-2 Division (xordiv) -> 5. 32-bit CRC Generated -> 6. Codeword Re-division at Receiver -> 7. Syndrome Zero Check.
Software & Stack Used | Backend: Python 3, Flask REST API, Flask-CORS. Frontend: Vanilla HTML5, CSS3 (Warm Monotone Single-Viewport), JavaScript Fetch API. Tools: VS Code, Git, Chrome.
Input / Test Data | Supports direct binary streams, raw log text messages, and full industrial .log / .txt files (10 pre-built demo reports provided in Downloads).
Final Output | Calculated 32-bit CRC, Hex digest (0x4964A71B), complete bitwise step-by-step audit trail, and instant binary ACCEPT (0^32) or REJECT chip.

## Slide 3
SLIDE 3 • CRC MATHEMATICS
Operating Principle of CRC: Mathematical Foundations
SLIDE 03
POLYNOMIAL MAPPING
1. Polynomial Mapping & GF(2)
• Bitstream is treated as polynomial coefficients over Galois Field GF(2).
• Example: 'A' = 01000001₂ -> P(x) = x⁶ + 1.
• Arithmetic Rule: Addition and subtraction are identical to bitwise XOR (⊕).
• Zero Carry/Borrow: Enables line-rate single-cycle hardware execution.
DIVISION MECHANICS
2. Modulo-2 Division & 32-Zero Padding
• Sender appends 32 zeros to data: M(x) · x³².
• Long division performed with 33-bit Generator G(x).
• If current bit is 1, XOR with divisor; if 0, shift 1 bit right.
• M(x) · x³² = Q(x)·G(x) ⊕ R(x). Remainder R(x) is the 32-bit CRC.
SYNDROME INVARIANT
3. Codeword & Receiver Syndrome Proof
• Codeword Transmitted: T(x) = M(x) · x³² ⊕ R(x).
• Algebraic Invariant: T(x) = Q(x)·G(x) ⊕ R(x) ⊕ R(x) = Q(x)·G(x).
• Receiver Division: T'(x) mod G(x) = R'(x).
• Decision Rule: If R'(x) == 0³² -> ACCEPT (No Error); else REJECT.

## Slide 4
SLIDE 4 • PYTHON IMPLEMENTATION
Python Implementation of CRC (crc_checker.py)
SLIDE 04
HANDWRITTEN PYTHON LOGIC
Core Algorithmic Functions (No Black-Box / No zlib)
def ascii2binary(text):
return ''.join(f'{ord(c):08b}' for c in text)
def xordiv(dividend, divisor):
d, m = list(dividend), len(divisor) # 33 bits
for i in range(len(d) - m + 1):
if d[i] == '1':
for j in range(m):
d[i+j] = '1' if d[i+j] != divisor[j] else '0'
return ''.join(d[-(m-1):]) # Returns last 32 bits
def compute_crc(text):
return xordiv(ascii2binary(text) + '0'*32, get_divisor())
def verify(text, received_crc):
return xordiv(ascii2binary(text) + received_crc, get_divisor()) == '0'*32
Input Type | Processing Flow in Code
Binary Input | Binary String -> Direct Length Validation -> xordiv() -> 32-bit CRC
Text Input | Text String -> ascii2binary() (8-bit ASCII) -> Append 32 Zeros -> xordiv() -> CRC
File Input | File Upload -> FileReader (JS) -> utf-8 text -> ascii2binary() -> xordiv() -> CRC
FUNCTION SPECIFICATION
Function Interface & Data Flow
• Input Passed: UTF-8 log message string or file buffer.
• Processing: Bit-by-bit Modulo-2 long division against session divisor.
• Output Returned: 32-bit CRC string, Hex checksum, intermediate steps.
• Invariant: Both compute_crc() and verify() call the identical get_divisor().

## Slide 5
SLIDE 5 • DASHBOARD DETAILS
Dashboard & Application Details (User Perspective)
SLIDE 05
Aspect | System Details & Implementation
Software Used | Flask 2.3+ REST backend (Port 5000), Vanilla JS frontend, Modern HTML5/CSS3 with Warm Monotone palette.
Intended Users | Industrial plant operators, SCADA instrumentation engineers, edge gateway monitors, QA compliance auditors.
Dashboard Inputs | Original log textarea, file upload (.txt/.log), random telemetry generator, received log textarea, received CRC input.
Dashboard Outputs | Calculated 32-bit CRC, Hex digest, step-by-step binary/padding/remainder calculations, ACCEPT/REJECT status badge.
DASHBOARD-TO-CODE-TO-DASHBOARD PIPELINE
Complete End-to-End System Execution Flow (Guideline Flowchart)
User Input (Text/File Upload) ➔ Dashboard State ➔ POST /api/compute (Fetch API) ➔ ascii2binary() ➔ xordiv() ➔
➔ Return CRC & Steps JSON ➔ Live Dashboard Telemetry Rendering (Steps 1 to 5) ➔
➔ Receiver Re-ingestion ➔ POST /api/verify ➔ Codeword Remainder Division ➔ Result Chip [✓ ACCEPT / ✗ REJECT]

## Slide 6
SLIDE 6 • TESTING MATRIX
Comprehensive Testing & Test Cases Matrix
SLIDE 06
Test ID | Input Data | Operation | Expected Result | Actual Result | Status
TC-01 | Binary: 101100101 | CRC-32 Modulo-2 | 32-bit CRC generated | Correct CRC calculated | PASS
TC-02 | Text: [TURBINE_01] RPM:3450 | CRC Computation | 32-bit CRC + Hex returned | 0x367B4724 displayed | PASS
TC-03 | File: Report_01_Turbine.log | File Upload CRC | Complete file CRC computed | Steps 1-5 displayed | PASS
TC-04 | Modified: RPM:3450 -> RPM:3451 | Error Detection | Non-zero Remainder -> REJECT | Remainder != 0 (REJECT) | PASS
TC-05 | Unmodified: Valid Log + CRC | Verification Check | Remainder = 0^32 -> ACCEPT | Remainder = 0 (ACCEPT) | PASS
TEST COVERAGE SUMMARY
Mandatory Test Requirements Verified (Guideline Section 6)
✓ Valid binary bitstream input tested | ✓ UTF-8 string telemetry tested | ✓ Real industrial .log/.txt files tested
✓ Single-bit flipped error detected (REJECT) | ✓ Unmodified original log verified authentic (ACCEPT)

## Slide 7
SLIDE 7 • ENGINEERING CHALLENGES
Errors & Engineering Challenges Faced (Problem -> Reason -> Solution -> Learning)
SLIDE 07
Problem / Challenge | Root Cause | Engineering Solution | Learning Outcome
Polynomial Bit Length | Using 32-bit divisor for 32-bit CRC caused degree underflow. | Generated 33-bit divisor with MSB=1 and LSB=1 (degree 32). | Understood that degree-n polynomial requires n+1 coefficients.
Modulo-2 Long Division | Integer division propagates carries, producing arithmetic quotient. | Built handwritten bitwise XOR loop shifting without carries/borrows. | Mastered Galois Field GF(2) long division algorithms.
Divisor Synchronization | Sender & receiver generated different random polynomials. | Created singleton get_divisor() fixed for entire session in memory. | Learned session-level state management and protocol parity.
Single-Screen Layout | Long step outputs created ugly outer window scrolling. | Engineered 2-row CSS grid with internal 6px custom scrollbars. | Mastered responsive viewport budgeting without layout thrashing.

## Slide 8
SLIDE 8 • FEATURES & DEMO GUIDE
Additional Features & Live Demonstration Sequence
SLIDE 08
UNIQUE SYSTEM HIGHLIGHTS
Working Additional Features
• Session-Fixed 33-Bit Generator: Singleton generator shared across all endpoints via GET /api/divisor.
• 10-Report Demo Pack: Pre-populated industrial test reports (.log/.txt) in Downloads for instant live testing.
• Step-by-Step Telemetry Audit: Full visibility into ASCII binary, 32-zero padding, divisor, remainder, and hex.
• Dual-Row Single Viewport UI: No page overflow; internal 6px subtle scrollbars; instant random log generator.
DEMONSTRATION PLAYBOOK
Live Demonstration Sequence (Guideline Section 12)
Step 1 (PPT): Explain Problem, Math & Architecture (Slides 1-4).
Step 2 (Dashboard): Upload Report_01_Turbine.log & click Compute CRC.
Step 3 (Code): Trace ascii2binary() and xordiv() in crc_checker.py.
Step 4 (Dashboard): Demonstrate Accept (0^32) & Reject (modify 1 character).
Step 5 (Summary): Conclude with integrity guarantees & Viva defense.
THREE-WINDOW DEMONSTRATION READY
Live Demo Windows Prepared: 1. PowerPoint Presentation | 2. Dashboard (http://localhost:5000) | 3. Python Code (VS Code)

## Slide 9
SLIDE 9 • VIVA DEFENSE
Viva Voce & Technical Defense Preparation
SLIDE 09
MATHEMATICAL VIVA QUESTIONS
Key Mathematical & Concept Questions
Q1: What is CRC & why is it used?
-> Cyclic Redundancy Check; detects burst errors in bitstreams using polynomial long division over GF(2).
Q2: Why 33-bit divisor for 32-bit CRC?
-> A degree-32 polynomial has 33 coefficients. Dividing by degree-32 strictly leaves a remainder of degree <= 31 (32 bits).
Q3: Why is XOR used instead of subtraction?
-> In GF(2) arithmetic, addition and subtraction are identical to bitwise XOR with no carries or borrows.
Q4: Can CRC correct errors?
-> CRC is primarily for error detection. In pure form it flags corruption; error correction requires FEC (e.g. Reed-Solomon/Hamming).
ENGINEERING VIVA QUESTIONS
Implementation & Verification Questions
Q5: How is text converted before CRC calculation?
-> Each character is converted to its 8-bit ASCII binary representation via ascii2binary() and concatenated.
Q6: How does the receiver detect an error?
-> Codeword T'(x) = Data + Received CRC is divided by G(x). If remainder is 0^32 -> ACCEPT; else REJECT.
Q7: What happens if one bit is changed?
-> The polynomial M'(x) differs from M(x), resulting in a non-zero syndrome remainder vector R'(x) != 0.
Q8: What error types are 100% detected?
-> All single-bit errors, all double-bit errors, and all burst errors <= 32 bits.

## Slide 10
SLIDE 10 • FINAL SUMMARY
Product Summary & Key Learning Outcomes
SLIDE 10
SYSTEM SPECIFICATIONS
Product Summary & Deliverables
• Developed Product: Industrial Machine Log Integrity Checker (Product 8).
• Supported Input Types: Raw binary bitstreams, UTF-8 text strings, and industrial .log / .txt telemetry files.
• Supported CRC Algorithm: Pure Modulo-2 XOR CRC-32 with session-fixed 33-bit generator polynomial.
• Error Detection Capabilities: 100% single bit, 100% double bit, 100% bursts <= 32 bits, 99.99999997% longer bursts.
• Software Stack: Python 3, Flask REST API, Vanilla HTML5/CSS3/JS, Warm Monotone Single-Screen UI.
ACADEMIC & PRACTICAL LEARNING
Key Learning Outcomes (OS & Computer Networks)
1. Protocol Parity: Implemented synchronized sender-receiver telemetry pipelines using shared algebraic invariants.
2. Bitwise Computing: Built low-level bit shifting and XOR operations without relying on opaque external libraries (zlib).
3. Network Error Detection: Understood why polynomial division surpasses additive checksums in noisy transmission channels.
4. Full-Stack Integration: Integrated Flask REST endpoints with real-time UI telemetry and FileReader APIs.
5. Teamwork & Collaboration: Successfully divided roles across architecture, algorithms, UI, backend, and QA testing.